## Slide 1: Concurrency – All the way down
Ofek Shilon
C++Online 2026

## Slide 2: Example Program
Store1: NEW  data
Load1: reg1  ready
Store2: TRUE  ready
Load2: reg2  data
Branch1: if !reg1 goto Load1
Writer Core
Reader Core

## Slide 3: Sequential Consistency (SC)
Store1: NEW  data
Load1: reg1  ready
Store2: TRUE  ready
Load2: reg2  data
Branch1: if !reg1 goto Load1
Writer Core
Reader Core

## Slide 4: Sequential Consistency (SC)
Store1: NEW  data
Load1: reg1  ready=true
Store2: TRUE  ready
Load2: reg2  data

## Slide 5: Sequential Consistency (SC)
Store1: NEW  data
Load1: reg1  ready=false
Store2: TRUE  ready
Load2: reg2  data
Load1: reg1  ready=false
Load1: reg1  ready=false
Load1: reg1  ready=true

## Slide 6: Initial System Model
Core
Core
Main Memory
L2/L3: Shared Caches
L1:
Private Cache
L1: Private Cache

## Slide 7: Initial System Model
Caches + Memory
Core
Core

## Slide 8: Hardware Optimizations
That mess with perceived order

## Slide 9: #1: FIFO write buffers
Caches + Memory
Core
data  NEW
Write buffer

## Slide 10: #1: FIFO write buffers
Caches + Memory
Core
data  NEW
Core
data?
data?
NEW
OLD

## Slide 11: #1: FIFO write buffers
Caches + Memory
Core
data  NEW
Core
ready  TRUE
data? OLD
ready? FALSE

## Slide 12: #1: FIFO write buffers
Caches + Memory
Core
data  NEW
Core
ready  TRUE
data? NEW
ready? FALSE

## Slide 13: #1: FIFO write buffers
Caches + Memory
Core
Core
ready  TRUE
data? NEW
ready? TRUE

## Slide 14: Total Store Order (TSO)
All cores agree on the order of stores-initiated-by-a-given-core
Implemented in all x86-64 systems

## Slide 15: #2: Coalescing write buffers
Coalesce writes to the same cache line

## Slide 16: Cache Lines
Core
Memory
L1 Cache
deadcafe
deadcafe
deadc9fe
L1 Cache
deadcafe
Core

## Slide 17: #2: Coalescing write buffers
Coalesche writes to the same cache line

## Slide 18: #2: Coalescing write buffers
B  1
C  1
Caches + Memory
Core
A  1

## Slide 19: #2: Coalescing write buffers
Caches + Memory
Core
A, B  1
C  1

## Slide 20: #2: Coalescing write buffers
C  1
Caches + Memory
Core
Core
B  1
A? 0 B? 0 C? 0
A  1

## Slide 21: #2: Coalescing write buffers
Caches + Memory
Core
Core
B  1
A, C  1
A? 0 B? 0 C? 0

## Slide 22: #2: Coalescing write buffers
Caches + Memory
Core
Core
B  1
A? 1 B? 0 C? 1

## Slide 23: #2: Coalescing write buffers
Caches + Memory
Core
Core
dummy? 0 data? OLD ready? FALSE
ready  TRUE
data  NEW
dummy  1

## Slide 24: #2: Coalescing write buffers
Caches + Memory
Core
Core
data  NEW
dummy  1 ready  TRUE
dummy? 0 data? OLD ready? FALSE

## Slide 25: #2: Coalescing write buffers
Caches + Memory
Core
Core
data  NEW
dummy? 1 data? OLD ready? TRUE

## Slide 26: #3: Invalidate queues
Core
Memory
L1 Cache
deadcafe
deadcafe
deadc9fe
L1 Cache
deadcafe
Core

## Slide 27: #3: Invalidate queues
Invalidate
queue
Core
L1 Cache
L1 Cache
deadcafe
Core
deadcafe
deadc9fe
data? deadcafe
data? deadc9fe

## Slide 28: #4: non multi-copy atomicity
Core
L1 Cache
OLD
NEW
L1 Cache
OLD
Core
Core
L1 Cache
OLD
?

## Slide 29: #5: Out-of-Order Execution
Load2’: reg2’  data (=OLD)
Store1: NEW  data
Load1: reg1  ready
Store2: TRUE  ready
Load2: reg2  data
Writer Core
Reader Core
(=TRUE)
(=OLD!)

## Slide 30: #6: Speculative Execution
if (ready) {
local_data = data
…
Memory/Caches
TRUE
OLD

## Slide 31: Counter Measures
Fences, load-acquire, store-release, RMW

## Slide 32: Fences: Full
x86/64: MFENCE (Memory Fence)
ARM: DSB (Data Store Barrier)
  Drain store buffer
  Wait until previous stores are visible everywhere and previous loads retired
  Acts as a reorder/speculation barrier
Safest + most expensive

## Slide 33: Fences: Full
x86/64: MFENCE (Memory Fence)
ARM: DSB (Data Store Barrier)
ARM: DMB SY (Data Memory Barrier, System-wide)
Operation:
  Enforce ordering, not completion
  At: Reorder buffers, write buffers, load queues
Cheaper alternative with mostly-compatible semantics
store
load
store
load

## Slide 34: Fences: Store
x86/64: SFENCE
  Controls completion
  Drain store buffer, stall until older stores are visible everywhere
  Reorder barrier
  Regular stores are already ordered! Empty pessimization
  Impacts special non-cached store instructions (MOVNT*).
store
store

## Slide 35: Fences: Load
x86/64: LFENCE
  Block a younger read from issuing until all older reads have completed
    Completed = issued + resolved cache misses + retired
  Block speculative execution past the fence
    only in recent generations – 2018+ (since Spectre)
load
load

## Slide 36: ARM: Acquire / Release
dmb ld
dmb st
store
load
store
load
load
store

## Slide 37: ARM: Acquire / Release
dmb ld
dmb st
store
load
store
load
ldar – Load Acquire
stlr – Store Release
load
store

## Slide 38: ARM: Acquire / Release
Store1: NEW  data
Load1: reg1  ready
Load2: reg2  data
Branch1: if !reg1 goto Load1
Reader Core
Store2: TRUE  ready
Writer Core
Store2: stlr ready, TRUE
Load1: ldar reg1, ready

## Slide 39: ARM: Acquire / Release
Store1: NEW  data
Load2: reg2  data
Branch1: if !reg1 goto Load1
Store2: stlr ready, TRUE
Load1: ldar reg1, ready
int data = 0;
std::atomic<bool> ready = 0;
int read() {
while
(!ready.load(memory_order_acquire));
return data;
}
void write() {
data = NEW;
ready.store(true,
memory_order_release);
}

## Slide 40: C++ std::memory_order
For stores:
  memory_order_release
For loads:
  memory_order_acquire
  (==memory_order_consume)
For Read-Modify-Write (RMW) ops, such as +=:
  memory_order_relaxed: no order guarantees
  memory_order_acq_rel: acquire AND release
For all:
  memory_order_seq_cst: full sequential consistency
    ?

## Slide 41: Read-Modify-Write
C++ atomic<> ops:
  +=, -=, &=, |=, ^=
    fetch_add(), fetch_sub(), fetch_and(), fetch_or(), fetch_xor()
  exchange()
  compare_exchange_weak(), compare_exchange_strong()
X86-64: LOCK prefix
ARM: LL/SC
  + dedicated instructions, in ARM v8.1+

## Slide 42: Read-modify-write: x86-64
Core
L1 Cache
L1 Cache
deadcafe
deadcafe
deadc9fe

## Slide 43: Read-modify-write: x86-64
Core
L1 Cache
L1 Cache
deadcafe
L1 Cache
beadcafe
deadcafe
deadc9fe

## Slide 44: Read-modify-write: ARM
Core
L1 Cache
X
deadcafe
deadc9fe
LDXR
STXR

## Slide 45: Read-modify-write: ARM
Core
L1 Cache
X
deadcafe
LDXR
STXR
L1 Cache
beadcafe
Core
STR

## Slide 46: Read-modify-write: ARM
Core
L1 Cache
X
deadcafe
LDXR
STXR
  compare_exchange_weak(), compare_exchange_strong()

## Slide 47: Read-modify-write: ARM
LDXR/STXR extension:
  LDAXR – load-acquire exclusive register
  STLXR – store-release exclusive register
  Additionally enforce acquire/release ordering, same as LDAR/STLR
  Necessary to actually be usable in locks
Riddle: why is the exclusive monitor needed?

## Slide 48: Cache Coherence Protocols
Cache line states:
Valid
Invalid

## Slide 49: Cache Coherence Protocols
Cache line states:
Modified
Invalid
Exclusive
Shared
MESI
(MESIF)
(MOESI)

## Slide 50: Summary
Different cores can have different views of memory because:
  Reasons
  More reasons
  Other reasons
Software solves these problems by:
  Fences
  RMW
  OS level locks: futexes, mutexes etc.

## Slide 51: Final Thoughts
Good chance you care only about x64 (?)
Doubtful the C++ standard phrasing is any simpler.

## Slide 52: Thanks for listening!
Questions and comments are welcome, in gather town or discord.
Ofek Shilon
OfekShilon @

## Slide 54: Resources

## Slide 55: NT writes, Write-Combine Buffers
(Canonical) Example use case: zero a memory page
Telling the processor it is about to overwrite full cache lines
WCB: collect multiple writes before sending to the cache coherency system
Avoid the inefficient dance of RFO (Read-For-Ownership) request + modification + writeback.
MOVNT* instructions, do not undergo the usual coherency route – may be visible only some time in the future.

## Slide 56: Fences: Implicit
Instructions with some order-serialization side effects:
  x86/64:
    CPUID, IRET, RSM, LOCK *, …
  ARM:
    MSR, MRS, ERET, SVC, HVC, SMC …